## Slide 1: Measuring Pulse Width with an Autocorrelator
Katya Mikhailova, Mentor: Daniel Rolles
Funded by NSF

## Slide 2: Background/Motivation Introduction
Goal: create molecular movies of light-induced molecular reactions to be able to visualize the dynamics of the reaction
How: use a femtosecond laser pulses to trigger the reaction and take snapshots of the reaction
  pump-probe experiment

## Slide 3: Pulse Width Introduction
Important to characterize the pulse duration
  “shutter speed”
  laser pulse reference
Can be measured using an autocorrelator setup
  why use an autocorrelator?
[1]
Notes: detector is delay line anode

## Slide 4: Chirp Introduction
Time dependent wavelength
Causes inaccurate pulse width measurements in autocorrelator
Want to be able to detect if a pulse is chirped
[2]
Notes: detector is delay line anode

## Slide 5: Autocorrelator Setup
delay stage
crystal
spectrometer
move delay stage to change if pulses overlap in crystal
spectrometer detects the probe byproduct
non-linear process in crystal “uses up” some of the probe
pump
probe
Notes: detector is delay line anode

## Slide 6: Step 1) Find time zero How to Get Pulse Width
what is time zero?
Notes: detector is delay line anode

## Slide 7: Step 1) Find time zero How to Get Pulse Width
spatial overlap by aligning optics
temporal overlap by moving delay stage
will see max depletion
spectrometer signal
Notes: detector is delay line anode

## Slide 8: Step 2) Take measurements How to Get Pulse Width
take measurements at different delays moving through time zero
take multiple runs
Amplitude
Wavelength
250 255 260 265 270 275 280
Notes: detector is delay line anode

## Slide 9: Step 3) Analyze data How to Get Pulse Width
plot sum of spectra over region vs delay
  can use peaks
Notes: detector is delay line anode

## Slide 10: Step 3) Analyze data How to Get Pulse Width
plot sum of spectra over region vs delay
  can use peaks
  or area
Notes: detector is delay line anode

## Slide 11: Step 3) Analyze data How to Get Pulse Width
plot sum of spectra over region vs delay
  can use peaks
  or area
fit a gaussian to deconvolute and get pulse width
Notes: detector is delay line anode

## Slide 12: Crystal type FLAME 266 nm Uncompressed
can analyze different powers and different crystals
look into band gap of different crystals
thicker crystals have greater PW
increase in PW with power
Notes: detector is delay line anode

## Slide 13: Peak vs Area FLAME 266 nm Uncompressed
can analyze different powers and using peak vs area values
Difference appears to be within error
  about 10 fs
Notes: detector is delay line anode

## Slide 14: Peak vs Area PULSAR 266nm Uncompressed
see a huge difference between the area and peak measurements
  50 fs to 100 fs difference
Area starts depleting before peak
  chirp?
Notes: detector is delay line anode

## Slide 15: Chirp Evidence in Spectrometer Data PULSAR 266nm Uncompressed
can see the peak shift as the different wavelengths come in at different speeds
  higher wavelengths faster
follow the outline of the average spectra shape
Notes: detector is delay line anode

## Slide 16: Autocorrelator 2D Spectrogram PULSAR 266 nm Uncompressed
Peak shifted to higher wavelength
Peak shifted to lower wavelength
clearly see a diagonal signature in the depletion
clearer visual of chirped pulse
Notes: detector is delay line anode

## Slide 17: PULSAR 266nm vs FLAME 266nm Spectrogram
clearly see a diagonal signature in the depletion
  Expect vertical slope when unchirped
the FLAME data appears to have less of a slope compared to PULSAR
PULSAR
FLAME
Notes: detector is delay line anode

## Slide 18: Conclusion
The autocorrelator is a promising method for measuring pulse width
Can be used as a chirp detection tool
  Literature shows can extract FROG traces
Future work: implementing noise/background subtraction techniques

## Slide 19: Acknowledgements
Daniel Rolles
Zane Phelps
Surjendu Bhattacharyya
Anbu Venkatachalam
James R. Macdonald Laboratory
Kansas State University
National Science Foundation

## Slide 20: Thank you for your time! Questions?

## Slide 21: References
Homann, C., Krebs, N. & Riedle, E. Convenient pulse length measurement of sub-20-fs pulses down to the deep UV via two-photon absorption in bulk material. Appl. Phys. B 104, 783 (2011). https://doi.org/10.1007/s00340-011-4683-0
[2] Hoyt, C., A. Schaffer, C. Fredrick, N. Parks, A. Thomas, D. Mohr and R. Jones. “Ultrafast Optics with a Mode-locked Erbium Fiber Laser.” (2015).
K. Ogawa and M. D. Pelusi. High-sensitivity pulse spectrogram measurement using two-photon absorption in a semiconductor at 1.5-µm wavelength. Opt. Express 7, 135-140 (2000).
https://doi.org/10.1364/OE.7.000135
[1] Peng, Jiahui. “Tunable Femtosecond Pulse Generation and Applications in Raman Micro-Spectroscopy.” (2021).
Trebino R., Zeek E. The Autocorrelation, the Spectrum, and Phase Retrieval. In: Frequency-Resolved Optical Gating: The Measurement of Ultrashort Laser Pulses. Springer, Boston, MA (2000). https://doi.org/10.1007/978-1-4615-1181-6_4
Paschotta, Rudiger. Chirp. RP Photonics. https://www.rp-photonics.com/chirp.html
Paschotta, Rudiger. Autocorrelators. RP Photonics. https://www.rp-photonics.com/autocorrelators.html

## Slide 22: Pulse Width (PW) Measurement Pulse Width for 200 nm from PULSAR
get PW of 151 +/- 13 fs
  expect 140 fs
very noisy
Notes: detector is delay line anode