## Slide 1: Characterizing a Parallel plate Imaging Deflector
Anjali Filinovich

## Slide 2: Understanding laser-molecular ion interactions using momentum imaging
Measure final position and time of flight of each fragment
Calculate momentum information, learn about fragmentation process
My project does not deal with the spectrometer field.
Ultrafast
laser
4.5 keV HD+
ion beam
Imaging deflector
Time- and position-sensitive detectors
Neutrals
H+
Faraday cup
Spectrometer
Adjustable height
D+

## Slide 3: Understanding laser-ion interactions using momentum imaging
Examining fragmentation of HD+ resulting from its interaction with a 790 nm laser pulse.
H+ + D Dissociation channel
McKenna, J., et al. Phys. Review A. 80 (2009).
H+ + D vibrational states
Notes: In this graph, you can see the signature of the different vibr states of HD+

## Slide 4: Goal
There is a discrepancy between model (ideal) and real parallel plate deflector fields.
Distortions in the real deflector field decrease the resolution of position and TOF data.
2-detector measurement
with imaging deflector
1-detector measurement
without imaging deflector
Real parallel plate deflector field lines
Ideal parallel plate deflector field lines
Notes: With defl off, we could resolve different vibrational levels, w defl on, high defl voltage distorts imaging,vibr. structure blurs
My contribution to this project has been… then goal
The addition of a second target made it necessary to use an imaging deflector, causing some probs
Looking for vibrational energies of HD+ which acts kind of like a harmonic oscillator. Peaks are those energies. Not as clear in fig. 2
Higher voltage used to deflect different masses means more fringe field effects
Ions flying off of deflector axis
  The fringe field of deflector causes distortions
  Decrease in resolution of measurements

## Slide 5: Goal
Characterize imaging deflector to enable retrieval of momentum information.
  Use simulation to represent experimental data (real deflector field)
  Generate analytical formula to fit simulated data
    - The basis of this analytical formula is the model of an ideal parallel plate deflector
  Use analytical formula to find position and time of flight without deflector distortions

## Slide 6: Model
… or simply put,
+x
q = charge
Ez =
vix = dissociation velocity in x-direction
TOF = Time of flight
Notes: X should have a lot of deflection, Y should have no deflection, z should have a time delay

## Slide 7: Model
… or simply put,
Characterize distortion in position by fitting the model to simulated data.
q = charge
Ez =
vix = dissociation velocity in x-direction
TOF = Time of flight
Notes: X should have a lot of deflection, Y should have no deflection, z should have a time delay

## Slide 8: Methods
Generate initial conditions for simulation in Matlab
Collect time of flight, impact position, and other ion trajectory data in Simion
Compare simulated result to model, modify model equation and add correction terms to describe the distortion due to the deflector field.
Ion trajectories
Deflector
Example of an ion trajectory in Simion
Notes: Simion solves Laplace equation

## Slide 9: Results
Characterize distortions in the
  x - direction
  z - direction (TOF)
  y - direction
Neutrals
H+
D+
x
y
z
Notes: How motion in these directions effects our measurement of position, TOF, and momentum

## Slide 10: Correcting x-position model
Compared simulation results to model results, corrected model
2nd order correction
Position resolution of imaging setup: 0.25 mm
Notes: Show coefficients in F graph
We know our correction is good enough because the residuals are less than 0.2 mm.

## Slide 11: x-position correction coefficients
Plotting F vs Escl allows us to remove deflector distortions in position under a variety of initial conditions
Fit curves to find functional form of each coefficient
Notes: We plot F vs Escl because each fragment might have different Escl because of different initial conditions in the energy or the charge.

## Slide 12: Modeling distortions in TOF
Fit time delay
Residual is smaller than time resolution (0.2 ns) with second order fit
Notes: Show coefficients in F graph
We know our correction is good enough because the residuals are less than 0.2 mm.

## Slide 13: TOF model coefficients for different conditions
Fit curves to find functional form of each coefficient
Use analytic expression to remove distortions in TOF for a variety of initial conditions.
*Some negative values omitted in middle plot. See inset graph
Notes: Show coefficients in F graph

## Slide 14: Summary
Corrected x-position model, allowing us to remove distortions in x-direction.
Determined an analytic expression for TOF delay to remove distortions in TOF.
Distortions in the y-direction are small enough to neglect for now.

## Slide 15: Future Work
Fit F vs. Escl curves to describe corrections for different initial conditions
Compare fitted model to simulation results to ensure its accuracy. Test in x, y, and z directions.
Use fitting expressions to recover fragment momentum information from experimental data

## Slide 16: Acknowledgements and Thanks
K-State REU Faculty
Itzik Ben-Itzhak
Chandan Bagdia (postdoc)
Kim Coy
Loren Greenman
J.T. Laverty
The National Science Foundation
Kansas State University
"This material is based upon work supported by the National Science Foundation under Grant No. #2244539. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation."

## Slide 18: Discrepancies between model and Simion results
Notes: -

## Slide 19
Characterizing motion in y

## Slide 20: Defining terms
yf – measured final y-position
TOF – measured time of flight
viy – initial velocity in the y-direction that was input into Simion.
viyM – y-velocity calculated using yf/TOF
V –volts
vy –instantaneous y-direction velocity as ion flies
viy was varied from -5  +5 eV (±0.0309497 mm/ns)
Total KE varied from 15001505 eV.

## Slide 21
Correcting deflector length (l1)
Multiplying equation by correction factor
Both corrections fit the data equally well, but adding the correction factor in one place is much simpler.

## Slide 22: Semi-log (y) Fitting Factor vs Escl
*negative data ignored in F1 graph

## Slide 23: Characterizing effects of motion in y
For viy less than 5 eV, TOF deviation is less than 0.2 ns. The time resolution of our setup is 0.2 ns.
Percent error in velocity is around 2%.
Notes: How motion in y impacts measurements of y, TOF