## Slide 1: Nuts and Bolts Difference Frequency Generation (DFG) Beam Time 7/15/14
Josh Nelson
Derrek Wilson
Carlos Trallero

## Slide 2: Goals
Create DFG from signal and idler (OPA)
Confirm that a beam from DFG is produced

## Slide 3: OPA
Signal = 1000 – 1550 nm
Idler = 1600 – 2500 nm
Conservation of Energy and momentum give out signal and idler
OPA
Pump Beam
signal
idler

## Slide 4: DFG Process
Signal
Idler
DFG
Conservation of Energy
ωs – ωi = ωDFG
Conservation of Momentum
Ks – Ki = KDFG

## Slide 5: Setup for DFG
KLS
2 mJ, 2 KHz, 30 fs
800 nm
OPA
0.5 mJ for S + I
S
I
AgGaS2 (silver thiogallate)
DFG crystal
Germanium Window
I
DFG
S
Block
Power Meter

## Slide 6: Data
Showed Phase Matching
Signal = 1470 nm
Idler = 1750 nm
1/λs – 1/ λi = 1/λDFG
λDFG = 9200 nm
Energy Split: S = 83% I = 17%

## Slide 7: Data
Power after OPA = 1 W
Calcite aligned so that signal and idler lose overlap in time
Signal = 1450 nm
Idler = 1705 nm
1/λs – 1/ λi = 1/λDFG
λDFG = 9700 nm
Energy Split: S =66% I = 34%
Chart: Powers of variating setups
| DFG and Germanium | Germanium | Germanium and Calcite
 | 10.5 | 1.2 | 1
1.2 mW
1.0 mW
10.5 mW

## Slide 8: Conclusion/Future
Effectively demonstrated DFG procedure
Found the wavelength of DFG in which gives us the largest power
Future:
  Change setup to allow for better control over time overlap of signal and idler
  Use setup on HITS