## Slide 1: A New Design for a Tunable External Cavity Diode Laser
J. W. Lyons, M.D. Mendiola and B. D. DePaola

## Slide 2: An Abstract
“We have designed and built a robust tunable external cavity diode laser that is easily constructed from commercial components. It requires only minimal, low tolerance machining, allowing for increased streamlining and ease of construction. The design also allows for the most commons types of laser diode packages, adding versatility.”

## Slide 3: What does that really mean?
We wanted a laser that:
was cheap
was easy to make
was adaptable

## Slide 4: What’s the Laser For?
Using these for our MOTRIMS experiment
  MOT=Magneto Optical Trap
  RIMS= Recoil Ion Momentum Spectroscopy
We use this to directly observe the populations in energy levels

## Slide 5: A Short “MOT” Review
Lasers use doppler shift to cool atoms
Zeeman Effect provides location-dependent force for trapping (an “Optical Molasses”)

## Slide 6: A Short “RIMS” Review
A beam on Na+ ions are fired at Rubidium-87
Rb absorb an electron=momentum change
Number of ions at each location gives population count of energy levels

## Slide 7: Laser Construction
Coarse and fine control of diffraction grating
Control temperature
Simplify wiring
Accomodate other diodes

## Slide 8
Diffraction grating mounted on commercial mirror mount.
Grating-diode distance is finely controlled by a PZT.
Diffraction Grating
Large, Unregulated TECs
Aluminum Heat Sink
Redirection Mirror
PZT for Wavelength Tuning
Laser Diode, Temperature Sensors, Collimating Tube
Base Plate
Small, Regulated TECs

## Slide 9
Two TECs between to thermally regulate diode in feedback loop with controller.
Two lower, unregulated TECs cool the device generally.

## Slide 10
Diode ring contains a separate temperature sensor to produce a human-interpretable output.

## Slide 11
Most components are connected to SIP sockets soldered to a circuit board mounted above the plate.

## Slide 12
Sockets are wired on the board to a DIP socket, where a DB-9 can connect via ribbon cable.

## Slide 13
To accommodate different diodes, “keys” can be constructed and placed in an intermediary socket. This accounts for diode differences.

## Slide 15: Features
Very simple design
Only a small amount of machining required (all low tolerance)
Adaptable for many different diodes
Capable of very effectively regulating internal temperature
Easy to disassemble/reassemble for troubleshooting and maintenance
Additional mirror eliminates beam steering during tuning
Works with easy to use commercial modules

## Slide 16: Acknowledgements
Thank you to:
Dr. DePaola
Madilena
K-State
NSF